## Slide 1: Sources, Multimeters, and Transformers
M.V. Iordache, EEGR2051 Circuits and Measurements Lab, Fall 2020, LeTourneau University
See https://mviordache.name/EEGR2051 for more information.

## Slide 2: DC Power Supplies

## Slide 3: DC Power Supplies—Review
Consist of electronic circuits that convert the AC supply of the wall outlet to DC.
Typically, they can operate in
  constant voltage (CV) mode.
  constant current (CC) mode.
The internal resistance of DC power supplies is negligible.
  In CV mode, the source resembles an ideal source of voltage.
  In CC mode, the source resembles an ideal source of current.
A triple DC power supply.

## Slide 4: DC Power Supplies—Review
When using the power supply:
  Set the voltage limit . This will be the voltage in CV mode.
  Set the current limit . This will be the current in CC mode.
Let be the output voltage and the output current.
If the source powers a circuit requiring a current at the voltage , then the source operates in CV mode at .
If the circuit requires a voltage at the current , then the source operates in CC mode at .
At any time, either or .
Notes: cvcc.fig

## Slide 5: DC Power Supplies
Example: A DC power supply has and . Find the short-circuit current.
Ideally, the resistance of a short-circuit is zero.
Therefore, .
The curve indicates that when . The answer is .
Example: In the previous example, what is the open-circuit voltage?
An open circuit implies .
The curve indicates that when . The answer is .
Notes: cvcc.fig

## Slide 6: DC Power Supplies
Example: Assuming a CV/CC supply with V and A, find the maximum value of for which the load operates in CC mode.
By Ohm’s law, .
The equation describes a line of slope .
The maximum slope for which the line intersects the curve of the source in the CC region is
Notes: cvex.fig and cvcc4.fig

## Slide 7: Adjusting Current and Voltage
If the voltage of a DC source cannot be changed, a simple way to adjust the load current is with a rheostat.
A rheostat is a variable resistor rated for high power levels.
In a slide rheostat:
  Resistive wire wound around an insulating tube forms a resistor.
  Let X and Y be the resistor terminals.
  A slider, also known as wiper, slides on a conductive bar B while touching the resistive wire.
  By moving the slider left or right, it is possible to vary the resistance between B and X or B and Y.
B
slider
X
Y

## Slide 8: Adjusting Current and Voltage
A rheostat may be represented by the symbol of a variable resistor.
Let be the resistance of the rheostat, that is, the resistance between the points X and Y.
As the slider is moved from X to Y:
  The resistance between X and B is varied from to .
  The resistance between Y and B is varied from to .
B
slider
X
Y

## Slide 9: Adjusting Current and Voltage
When a load requires a small amount of current, a simple way to change its voltage is with a potentiometer.
A potentiometer is a variable resistor rated for low power levels.
A potentiometer has:
  A resistive track connected to the left and right terminals.
  A wiper connected to the middle terminal and attached to a rotating shaft.
The wiper touches the resistive track.
By turning the shaft, the resistance between the middle terminal and the right/left terminals is varied.
Resistive track
Wiper touching the resistive track
Images from https://commons.wikimedia.org/wiki/File:Electronic-Component-Potentiometer.jpg
and https://commons.wikimedia.org/wiki/File:Single-turn_potentiometer_with_internals_exposed,_oblique_view.jpg

## Slide 10: Adjusting Current and Voltage—Example
A source is connected in series with a load and a rheostat.
When the rheostat is adjusted to , the load current is .
To reduce the current to , the rheostat has to be adjusted to a value satisfying
The load voltage is .
At , the efficiency of the system is
A rheostat provides a simple but inefficient way of controlling current.
Notes: rh_ex.fig

## Slide 11: Multimeters

## Slide 12: Measurement Range
DMMs perform measurements within a prespecified range.
  For example, typical current ranges are 200 A, 2 mA, 20 mA, 200 mA, 2 A, 20 A.
The range indicates the maximum value that can be measured.
  For example, if the range is set to 20 mA and a current is to be measured, then the DMM will indicate OVERLOAD.
  To measure the current, the range must be changed to .
A range can be changed by pressing the arrow keys.
  When an arrow key is pressed, the DMM enters the MANUAL mode.
If the AUTO key is pressed, the DMM selects automatically the right range.
Notes: amp.fig

## Slide 13
DMMs typically have two current terminals:
  The terminal for low-current ranges (typically, below 1A).
  The terminal for high-current ranges (typically, above 1A).
Current Measurements
Notes: amp.fig

## Slide 14: Current Measurements
How to know which terminal the DMM uses when performing a current measurement?
A DMM in AUTO mode will measure the current of the low-range terminal.
A DMM in MANUAL mode will measure the current of the low-range terminal when the range is less than 1 A.
A DMM in MANUAL mode will measure the current of the high-range terminal when the range is over 1 A.
DMMs use the high-range terminal only when in MANUAL mode on a range above .
Notes: rh_ex.fig

## Slide 15: Current Measurements—Examples
A DMM has the following current ranges: , , , , , . A current in the range should be measured.
Solution 1: Use the low-range terminal and AUTO mode.
Solution 2: Use the low-range terminal, MANUAL mode, and the range.
Solution 3: Use the high-range terminal, MANUAL mode, and the range.
Assume now that the unknown current is in the range .
Solution: Use the high-range terminal, MANUAL mode, and the range.
Notes: rh_ex.fig

## Slide 16: The Loading Effect
Ideally, an instrument will not change the value of the variable it measures.
However, DMMs connected to a circuit act as additional circuit loads and change somewhat the currents and voltages they measure.
This is known as the loading effect.
In most cases, when a DMM is used correctly, the loading effect is not significant.
To avoid measurement error, it is necessary to determine whether a DMM loads considerably a circuit.
Notes: amp.fig

## Slide 17: The Loading Effect—Voltage Measurements
Example: Suppose that the voltage should be measured.
A voltmeter is electrically equivalent to a resistor of very large value (such as ).
Let be the internal resistance of the voltmeter.
Adding a voltmeter to the circuit is equivalent to adding a resistor to the circuit.
Notes: vloading.fig

## Slide 18: The Loading Effect—Voltage Measurements
Adding a voltmeter to the circuit is equivalent to adding a resistor to the circuit.
Notes: vloading2.fig

## Slide 19: The Loading Effect—Voltage Measurements
Before connecting the voltmeter,
.
After connecting the voltmeter,
.
The change in voltage is negligible only if is much larger than .

## Slide 20: The Loading Effect—Voltage Measurements
For example, assume , , and .
The actual value of is .
If , the measured will be .
If , the measured will be .
If , the measured will be .
If , the measured will be !

## Slide 21: The Loading Effect—Current Measurements
Example: Suppose that the current should be measured.
An ammeter is electrically equivalent to a resistor of low value (such as ).
Let be the internal resistance of the ammeter.
Adding an ammeter to the circuit is equivalent to adding a resistor to the circuit.
Note that is not a constant but depends on range and current terminal (whether the low-range or high-range terminal is used.)
Notes: aloading.fig

## Slide 22: The Loading Effect—Current Measurements
Adding an ammeter to the circuit is equivalent to adding a resistor to the circuit.
Notes: aloading2.fig

## Slide 23: The Loading Effect—Current Measurements
Before connecting the ammeter,
.
After connecting the ammeter,
.
The change in current is negligible only if is much smaller than .

## Slide 24: The Loading Effect—Current Measurements
For example, assume , , on the high range terminal, and on the low range terminal for the range.
The actual value of is .
The value of when measured on the high range terminal is .
The value of when measured on the low range terminal is .

## Slide 25: Ammeters—Review
The current of a component is measured by placing the ammeter in series with the component.
Example: The current of the resistor should be measured.
Notes: amp2.fig

## Slide 26: How to Measure Current—Example (Continued)
Step 1: Disconnect the resistor at one of its ends.
Notes: amp3.fig

## Slide 27: How to Measure Current—Example (Continued)
Step 2: Reconnect the resistor by means of an ammeter, so that the current to or from the resistor flows through the ammeter.
The ammeter shows a current .
Notes: amp4.fig

## Slide 28: How to Measure Current—Example (Continued)
Note that by interchanging the connections of the ammeter, the sign of the measured current changes: instead of .
Notes: amp4.fig

## Slide 29: How to Measure Current—Review
Ammeters are always connected in series.
An ammeter may not be connected across a component.
Otherwise, the ammeter will show an incorrect value and the ammeter fuse may get blown.
Note that when the fuse is blown, the ammeter indicates a zero current (since no current can flow through it).
Notes: amp4.fig

## Slide 30: How to Measure Current—Example (Continued)
In the previous example, the current of the resistor was .
The figure below shows an incorrect way to measure this current.
The measurement is wrong because the ammeter is in parallel, not in series.
Notes: amp5.fig

## Slide 31: How to Measure Current—Example (Continued)
Current cannot be measured across a wire.
If the green wire is removed, the DMM will display the correct value.
Notes: amp6.fig

## Slide 32: Transformers

## Slide 33: Transformers
Figure downloaded from http://en.wikipedia.org/wiki/Transformer
A transformer is an AC device that transfers energy between electrically isolated circuits by means of magnetically coupled coils of wire.
A transformer consists of several coils placed on the same magnetic core.
Power is applied to the primary coil of the transformer and is transmitted by means of the magnetic field to the other coils, which are called secondary coils.

## Slide 34: Transformers
Ideally,
where
  and are the rms values of the primary and secondary voltages.
  and are the rms values of the primary and secondary currents.
  and are the number of turns of the primary and secondary coils.
For example, if , , and , then .
For example, if , , and , then .
The symbol of a transformer is shown in the figure.
Typically, transformers transfer energy at different voltage levels; a transformer can reduce or increase the input voltage.
Notes: transf-e.fig

## Slide 35: Transformers
where
  , , , are the rms values of the primary and secondary voltages.
  , , , are the rms values of the primary and secondary currents.
  , , , are the number of turns of the primary and secondary coils.
Transformers may have more than one secondary coil.
Under simplifying assumptions, the operation of a transformer with secondary coils is described by the equations:
Notes: transf-e2.fig

## Slide 36: Clamp-on Ammeters
Clamp-on ammeters measure the current of a conductor without physical contact.
Some clamp-on ammeters use Hall sensors to measure the magnetic field generated by the current of the conductor. They can work with both DC and AC.
Other clamp-on ammeter operate on the principle of the transformer: the measured conductor forms the primary, while an internal coil forms the secondary. Such ammeters work only with AC.
Although very convenient for making rapid current measurements, clamp-on ammeters are limited to relatively high current levels.

## Slide 37: Clamp-on Ammeters
Current is measured correctly when the conductor goes between the two jaws of the instrument.
Jaws