## Slide 1: Phasors
Representing Sinusoidal Voltages and Currents in the Frequency Domain
M.V. Iordache, EEGR2053 Electric Circuits, Spring 2020, LeTourneau University

## Slide 2: Introduction
Suppose that a sinusoidal voltage is applied at time .
Any voltage or current could be found by solving a system of differential equations.
For example, is found by solving the system of equations:
Notes: cfig/rlc.fig

## Slide 3: Introduction
By solving the differential equations, we obtain having the following graph.
Notes: out-sine.png

## Slide 4: Introduction
Note that converges to the red curve.
The red curve is called steady-state response.
Notes: out2-sine.png

## Slide 5: Introduction
Often, we do not care about transients, but we only need the steady-state.
The steady-state response can be obtained without solving differential equations.
To find the steady-state response, we will use this simpler method:
  Convert the circuit to the frequency domain.
  Solve for the unknowns in the frequency domain.
  Convert the unknowns back to the time domain.

## Slide 6: The Frequency Domain
Up to this point we have worked in the time domain.
Let be a current or a voltage.
We say that is in the time-domain.
The frequency domain representation of is the complex-valued function
Note that is the complex number of magnitude and angle .
We also write as .
Example:
.

## Slide 7: The Frequency Domain—Notation
Note that is the unit vector in the direction of the imaginary axis.
From now on, to avoid confusion with currents, will be used in the place of .
So .
Example: is the complex number of real part 3 and imaginary part 4.
That is, and .
In the complex plane, is represented by
a vector of length ,
at an angle .
We write that .

## Slide 8: The Frequency Domain
In the time domain, the signal is a sinusoidal function.
In the frequency domain, the signal is a vector that rotates counterclockwise in the complex plane at an angular velocity .
Such rotating vectors are called PHASORS.
TIME DOMAIN
FREQUENCY DOMAIN

## Slide 9: Impedance
Assume a network with two terminals that has no independent sources.
A voltage will result in a sinusoidal steady-state current of the same frequency: .
In the frequency domain, these correspond to the phasors
and .
For a linear network, the ratio is a constant called impedance.

## Slide 10: Impedance
Since and , impedance is independent of time:
The impedance is a constant, not a phasor!
Only voltages and currents are phasors.
The impedance unit is Ohms [
Impedance resembles resistance; it could be viewed as an “AC resistance”.

## Slide 11: Impedance of Common Components
Resistors, capacitors, and inductors are represented in the frequency domain by their impedance.
Notes: cfig/impedances.fig

## Slide 12: Phasors—Abbreviated Notation
Assume all sources of a circuit have the same frequency.
Every phasor will differ from any other phasor only in magnitude and angle.
The term is common for all phasors.
From now on, we will drop the term.
will be abbreviated .

## Slide 13: Examples
Write V in the frequency domain.
  V.
Write mA in the time domain.
  mA.
Find the impedance of the network.
A.
.
V.
.

## Slide 14: Example
Assume V and V . Write the total voltage as a sinusoidal function of time.
V.
V.
V.
The angle ,
  where could be 0 or , depending on the quadrant.
In this case .
The angle is in a quadrant with .
Hence, V.
The final answer is
  V.