## Slide 1: Nodal Analysis
A General Method for Solving Circuits
M.V. Iordache, EEGR2053 Electric Circuits, Spring 2020, LeTourneau University

## Slide 2: An important formula
Nodal equations can be written quickly if you remember this formula:
Notes: sum/nodalpr

## Slide 3: Select a reference node
Any node may serve as a reference node.
The choice is arbitrary.
Nodal analysis finds node voltages with respect to the reference node.
A reference node will be denoted by REF, or by the electric-ground symbol.
Notes: sum/nodalpr

## Slide 4: Mark the reference node
The node at the bottom left corner was chosen as the reference.

## Slide 5: Identify the nodes of the circuit
The nodes are N1 … N6 and REF.

## Slide 6: Identify nodal voltages
Nodal analysis solves for node voltages with respect to REF.

## Slide 7: Identify the supernodes
A supernode is a network in which every node is connected to some other node by a source of voltage or by a component of known voltage.
A path must exist between any two nodes that goes only through branches containing sources of voltage or components of known voltage.
The network must be maximal; do not leave outside of the supernode a node that is connected to it by a source of voltage or a component of known voltage.
Include into the network all components connected between any two nodes of the supernode.

## Slide 8: Supernodes
This network is not a supernode: it does not include node 6, so it is not maximal.

## Slide 9: Supernodes
This is not the best way to define the supernode: it does not include and .
It is best to include the components connected between the nodes of the network.

## Slide 10: Supernodes
The circuit has two supernodes:
SN1 and SN2.

## Slide 11: Supernode voltages
For each supernode, select a node n.
Let be the voltage of node n.
Express the voltage of every other node of the supernode in terms of (by KVL).
Example: Select for SN1.
  ,
  ,
  .
Example: Select REF for SN2
  .

## Slide 12: Supernode voltages

## Slide 13: Write KCL
Write KCL for every supernode that does not contain the REF node.
Write KCL for every node that is not part of a supernode and that is not the REF node.
KCL for SN1:
KCL for node 2: