## Slide 1: DC Machines—Electrical Model and Equations
DC Motors and Generators
M.V. Iordache, EEGR3523 Mechatronics, Spring 2020, LeTourneau University

## Slide 2: Electric Model
The armature and field windings involve coils, and therefore have inductance.
However, we will perform a DC analysis involving average currents and voltages (that is, the DC components of the currents and voltages).
In DC, the ideal inductor is equivalent to a short circuit.
As for a practical inductor, its DC model is a resistor, corresponding to the resistance of the wire from which it is made.
The following electric symbol will be used for the armature.
  is the armature voltage.
  is the armature current.
Notes: presm/armature.fig

## Slide 3: Electric Model
The field windings will be represented by a resistor.
  is the field resistance.
  is the field voltage.
  is the field current.
The flux per field pole is:
where is a constant of the machine.
When the field poles are permanent magnets, there are no field windings and is a constant.
Notes: presm/armmdl.fig

## Slide 4: Electric Model
The armature windings model includes the armature resistance and the back electromotive force (back emf) .
  is the armature voltage.
  is the armature current.
The back emf is satisfies:
where
  is the flux per field pole.
  is the speed of the motor or generator.
  is a constant of the machine.
Notes: presm/fieldmdl.fig

## Slide 5: Permanent Magnet Machines
Since the back emf satisfies and is a constant, the back emf equation can be written in the simpler form
where is the torque constant.
The electromagnetic torque satisfies , which can also be written in the simpler form

## Slide 6: PM Motors
For a permanent magnet (PM) DC motor powered from a DC source , the equations , , and result in a linear torque-speed curve.
The higher the torque, the lower the speed!
If torque increases, current increases.
If current increases, back emf decreases.
If back emf decreases, speed decreases.
Notes: presm/dcmotor.fig

## Slide 7: PM Motors
The output power of a motor depends on the operating point.
  Note that . Substituting , , and , we obtain , which has the graph shown in the figure.
Notes: presm/dcmotor.fig

## Slide 8: PM Motors—Example 1
A permanent magnet motor has a stall torque of 0.05 Nm. The motor is connected to a source . Find the back emf at a torque of 0.01 Nm.
Since , the armature current depends on the torque.
  The higher the torque, the higher the current.
Since , the back emf is dependent on .
When the motor is stalled:
  The speed is .
  The stall torque equation is .
  Note that both and are constants of the motor.
Now .
When , .

## Slide 9: PM Motors—Example 2
A permanent magnet motor has a stall torque of 0.05 Nm. The motor is connected to a source . The armature resistance is . Find the speed at a torque of 0.01 Nm.
When the motor is stalled:
  The speed is .
  The torque equation is .
  Let us keep in mind that does not change; it is a PM motor constant.
When the motor operates at :
  .
  .
  .

## Slide 10: PM Generators
Generators are described by the same equations as motors.
Note, however, the different direction of the armature current!
Therefore, .
The torque applied to the generator is
The back emf is
Notes: presm/dcgen.fig

## Slide 11: PM Generators—Example
A permanent magnet generator has as armature resistance and powers a load . The load voltage is . Find the efficiency of the generator. For what load is the efficiency 50%?
Efficiency is not a constant of the machine but depends on the operating point.
Note that .
.
The output power is the power on the load:
The input power is the mechanical power applied to the generator:

## Slide 12: PM Generators—Example (Continued)
The efficiency is
If the efficiency is only , then .
Note that and will not have the same values as in the case of 90.9% efficiency.
Now
.

## Slide 13: DC Machines with Field Windings
The flux per field pole:
  Is constant when the field poles are permanent magnets.
  Is proportional to the current of the field windings when the field poles are electromagnets: , where is a constant.
If a machine has field windings:
Let . Note that is a constant of the machine. Then:

## Slide 14: DC Machines with Field Windings
The field and armature windings may be connected
  to different circuits for a separately excited motor or generator;
  in parallel for a shunt motor or generator;
  in series for a series motor (aka universal motor).
Notes: presm/motors.fig

## Slide 15: DC Machines with Field Windings
Considering the equations and , if is maintained constant, then the term will be a constant.
Therefore, for separately excited and shunt machines, is similar to the torque constant of the PM machines.
For series machines, however, since , the term cannot be a constant!

## Slide 16: DC Machines with Field Windings
Separately excited machines resemble PM machines.
Shunt motors tend to maintain constant speed.
Series motors work with both DC and AC supplies. Thus, they are known as universal motors.
  Series motors work well with AC because and are in phase (since they are identical).

## Slide 17: Shunt Machines
A shunt motor will not reverse the direction of rotation when the polarity of the supply voltage is changed.
  If , then and
  , so the torque does not change sign!
A shunt motor tends to maintain constant speed
(as long as the mechanical load is not excessive.)
  Note that
  For low torques, is small, and so .
  Therefore, .
  As long as the torque is not too big, the speed is
  independent of and equals .
Notes: presm/shunt.fig

## Slide 18: Shunt Machines—Example 1
A shunt generator outputs on a load . Assuming and , what is the efficiency of the generator?
Note the direction of for a generator.
  .
  .
The output power is .
The input power is .
The efficiency is .
Notes: presm/shunt2.fig

## Slide 19: Shunt Machines—Example 2
A shunt motor is powered at , has , draws at and at . Find the efficiency of the motor at and at .
.
At ,
  .
At ,
  .
Solving for and , we find
and .
Notes: presm/shunt.fig

## Slide 20: Shunt Machines—Example 2 (Continued)
The input power is .
The output power is . Substituting and :
.
The efficiency is .
At :
  .
At :
  .
Notes: presm/shunt.fig

## Slide 21: Shunt Machines—Example 3
Considering the motor of the previous example, what is the maximum efficiency? At what speed is the efficiency maximum?
In the previous example we derived that the efficiency is
.
.
.
Notes: presm/shunt.fig

## Slide 22: Series Motors
Series motors connect the field and the armature windings in series.
Series motors work with both DC and AC supplies. Thus, they are known as universal motors.
Notes: presm/series.fig

## Slide 23: Series Motors
Note that .
Therefore, the torque is .
A series motor will not reverse the direction of rotation when the polarity of the supply voltage is changed.
  If , then
  , so the torque does not change sign!
A series motor has a very high starting torque.
  Compared to other motors, the ratio of the starting torque and of
  the steady-state torque is much higher.
Series motors work well with AC because and are in
phase (since they are identical).
Notes: presm/series.fig

## Slide 24: Series Motors—Example
A series motor is powered at draws at and at . Find the efficiency of the motor at and at .
Note that . Substituting and , we obtain
.
At , .
At , .
Solving for and :
and .
The input power is .
The output power is .
Notes: presm/series.fig

## Slide 25: Series Motors—Example (Continued)
Since , the efficiency is
Note that .
At , .
At , .
Notes: presm/series.fig