## Slide 1: Single-Phase Induction Motors
M.V. Iordache, EEGR3523 Mechatronics, Spring 2020, LeTourneau University

## Slide 2: Introduction
AC motors rely on a rotating magnetic field.
  The rotor of a synchronous motor follows the field at the same speed.
  The rotor of an induction motor rotates because of the currents induced in it by the rotating field.
In a single phase motor, however, the magnetic field of the stator does not rotate.
For example, consider a single-phase motor with two stator poles.
Depending on the direction of the current, the
direction of the field is left-to-right or right-to-left.
The field pulsates, but does not rotate!
Additional stator poles connected to the same phase
will not make the field rotate.
Notes: docs/sum/shaded2.fig

## Slide 3: The Stator Field
Consider a single-phase stator in which all poles are connected to the same phase.
Let be the number of poles.
Let be the pole pitch angle (the angle between two adjacent poles).
Consider the flux density of the stator field inside of the rotor, near the surface of the rotor.
The flux density is sinusoidal, because the stator current is sinusoidal.
The coils of the stator poles are connected so that they produce fields in opposite directions.
So if near a stator pole, then near an adjacent stator pole.
Notes: docs/sum/shaded2.fig

## Slide 4: The Stator Field
The field at an angle could be approximated by
Let .
Note that
The first term, , describes a field that rotates in the direction of (clockwise in the figure).
The second term, , describes a field rotating in the opposite direction (counterclockwise in the figure).
Notes: presm/sfield.fig

## Slide 5: The Stator Field
We conclude that the stator field of a single phase motor consists of two rotating fields rotating in opposite directions.
The torques generated by the rotating fields are equal and in opposite directions.
Unless we ensure that one of the rotating fields is stronger, the motor will not start.
Once the rotor rotates, the torque produced by the field rotating in the same direction will be stronger, and the motor will run.
Notes: docs/sum/shaded2.fig

## Slide 6: Single-Phase Induction Motors
Single-phase induction motors, in order to be self-starting, create an additional phase.
Split-phase motors have:
  A main winding, that is always powered.
  A starting winding, that is connected only when the motor starts.
The starting winding is disconnected by a centrifugal switch when the rotor reaches a sufficiently high speed.
The starting winding has a higher resistance and a different reactance/resistance ratio.
In this way, the current of the starting winding is out of phase with the current of the main winding.
This creates a second phase and in this way a predominant rotating field.
Notes: docs/sum/shaded2.fig

## Slide 7: Single-Phase Induction Motors
Capacitor-start motors have:
  A main winding, that is always powered.
  A starting winding, connected in series with a capacitor.
The capacitor causes the current of the starting winding to be out of phase with the current of the main winding.
This creates a second phase and in this way a predominant rotating field.
Some motors disconnect the starting winding after the rotor has reached a predetermined speed.
Spring-loaded parts that are shifted off-center by the centrifugal force. They can turn off a switch at high enough speed.
Notes: docs/sum/shaded2.fig

## Slide 8: Single-Phase Induction Motors
Shaded-pole motors have:
  A short-circuited conductive strap (called shading band) wound on a portion of each pole.
  This creates a lag, and in this way a predominant rotating field that turns from the main face of the pole towards the shaded portion of the pole.
Shading band
Shading bands
Notes: docs/sum/shaded.fig

## Slide 9: Single-Phase Induction Motors
Single-phase induction motors are typically for relatively low power applications.
The rotor is typically of the squirrel-cage type.
Shading bands in a 4-pole stator.
Notes: docs/sum/shaded2.fig

## Slide 10: Electric Model of Single-Phase Induction Motors
The model resembles the per-phase model of polyphase induction motors.
There are differences because single phase motors have two rotating fields.
Notes: docs/online/sphase.fig

## Slide 11: Electric Model of Single-Phase Induction Motors
Let be the speed of the motor.
The slip with respect to the forward field is .
The slip with respect to the backward field is .
and are the stator resistance
and reactance, respectively.
and correspond to the
resistance and reactance,
respectively, of the rotor.
models that the magnetic
coupling of the rotor and stator is
imperfect.
Notes: docs/online/sphase.fig

## Slide 12: Electric Model of Single-Phase Induction Motors
Let , , , and be the rms values of , , , and .
The input average power is , where and denote the phase angles of and , respectively.
Recalling that reactances do not dissipate power,
is the stator copper loss.
is the
rotor power.
is the rotor copper loss.
is the
developed power.
Thus, the torque satisfies .
Notes: docs/online/sphase2.fig

## Slide 13: Example 1
The motor is powered at rms and . What is the maximum speed of the motor? Can the direction of rotation be reversed?
The synchronous speed is
The motor speed is .
The maximum speed is .
Practical motors cannot reach the
synchronous speed because the torque is
zero at the synchronous speed and the
motor has to overcome friction.
This motor turns counterclockwise and its
direction cannot be reversed.

## Slide 14: Example 2
A single phase induction motor has poles, is powered at rms and , has , , , , and . Find the torque and the efficiency when the motor has a slip of .
The slip of the rotor with respect to the backward field is .
Let
The total impedance of the motor is
The input current is rms.
Notes: p =4; xm = 200;x2 = 2; x1 = 2; r1 = 2; r2 = 1; v1 = 120; f = 60; s = 0.05; sb = 2-s; zf = par(j*xm/2, j*x2/2+r2/2/s); z_f = mpolar(zf), zb = par(j*xm/2, j*x2/2+r2/2/sb); z_b = mpolar(zb), z = r1+j*x1+zf+zb; z_t = mpolar(z), i1 = v1/z; p1 = abs(i1)^2*real(z); pd = abs(i1)^2*(1-s)*(real(zf)-real(zb)); n = 120*f/p*(1-s); w = n/60*2*pi; T = pd/w, eta = pd/p1, eta2 = (1-s)*(real(zf)-real(zb))/real(z)

## Slide 15: Example 2
The total rotor power is
The developed power is
The torque is
where .
Thus,

## Slide 16: Example 2
The efficiency is