## Slide 1: Sampled-Data Systems
Dealing with Systems that Have Both Discrete and Continuous-Time Modules
M.V. Iordache, EEGR4933 Automatic Control Systems, Spring 2019, LeTourneau University

## Slide 2: Sampled Data Systems
How to analyze systems that involve both continuous-time and discrete-time signals?
  Model A/D converters as ideal samplers.
  Model D/A converters as data hold systems.
  Use the starred transform.

## Slide 3: Ideal Samplers
An ideal sampler converts a continuous-time signal to a discrete-time signal so that
is the sampling interval.
is known as the starred transform of .
In the frequency domain, the ideal sampler converts to .

## Slide 4: Data Hold Systems
A data hold system converts a discrete-time signal to a continuous-time signal .
Let be the transfer function of the data hold.
(where .
For a zero-order hold,
when
    .

## Slide 5: Representing DT Signals in CT
A discrete-time (DT) signal can be applied to a continuous-time (CT) system.
First, it has to be converted to CT by a hold system .
Since the hold system is linear and time invariant:
  where .
So in the Laplace domain,
Traditionally, the DT signal is described by a distribution
With this kind of “input”:
Notes: It would be more intuitive to describe the hold system as a distribution that is applied to the incoming discrete-time signal. The distribution would be ∑𝛿(𝑛−𝑘)ℎ(𝑡−𝑘𝑇), mapping a discrete-time input 𝑚(𝑘) to a continuous time output 𝑚_𝑐 (𝑡). Traditionally, a distribution is used to map the continuous-time impulse response function ℎ(𝑡) to 𝑚_𝑐 (𝑡).

## Slide 6: The Starred Transform
How to calculate :
  Find .
  Let .
  Find .
  Let .

## Slide 7: The Pulse Transfer Function
The pulse transfer function of the transfer function is .
Let .
  is known as the impulse response of .
Let ; then, .
If is sampled and applied to G(s) and if is the output, then .
In practice, samples cannot be applied directly to , unless includes a data hold; a data-hold system must precede
If a data-hold is added, .

## Slide 8: The Pulse Transfer Function
If is sampled and applied to and if is the output, then .
If the samples are applied to , then the output satisfies , that is, .
If is applied directly to and is the output, .
In other words, .
This is because the sampled applied to is represented by , which is quite different from .

## Slide 9: MATLAB Example
Let be the sampling interval.
To find , write c2d(, , 'impulse')/.
Example: Find when .
s = tf('s'); % define the Laplace variable
T = 0.1; % indicate the sampling interval
% The starred transform is calculated with
c2d(exp(-3.2*T*s)/(s+3), T, 'impulse')*(1/T)
% The reason we divide by T is that c2d considers an impulse
% function 1/T*delta(k) instead of delta(k), and thus
% multiplies the starred transform by T.

## Slide 10: MATLAB Example
Example: Find in terms of .
% Define first the needed symbolic variables
s = sym('s'); k = sym('k'); t = sym('t');
% It is important that the symbolic solver knows that T is
% a positive real number.
T = sym('T', 'positive');
x = ilaplace(exp(-3.2*T*s)/(s+3)); % inverse Laplace transf.
xk = subs(x, 't', k*T); % substitute t with k*T to find x(kT)
xz = ztrans(xk); % find the z-transform
xz = collect(xz); % the result can be simplified
pretty(xz) % display the z-transform

## Slide 11: Diagrams with Analog and Digital Blocks
A signal Y(z) may be found with Mason’s formula.
This assumes the block diagram is converted to the z domain.
How to convert it:
  Merge s-domain blocks and split paths involving s-domain blocks so as to be able to replace every signal with a starred signal and s-domain blocks with starred TF blocks.

## Slide 12: Conversions to Discrete Time
In certain contexts, a continuous-time system may be substituted with a discrete-time system.
We will consider the following equivalence:

## Slide 13: Conversions to Discrete Time
Assume a zero-order hold model of D/A.
The DT equivalent of is
The DT equivalent of consists of with , , and
Note that the equivalent DT systems depend on T!

## Slide 14: MATLAB Example
Let be the sampling interval.
To find the DT equivalent of , write c2d(, , 'zoh').
s = tf('s'); % define the Laplace variable
T = 0.01; % indicate the sampling interval
% Find the DT equivalent of 1/(s*(s+15))
c2d(1/(s*(s+15)), T, 'zoh')
% To find a state space equivalent, the same procedure may
% be used.
sys = ss(1/(s*(s+15)); % find a state space representation
sysd = c2d(sys, T, 'zoh'); % convert sys to discrete time

## Slide 15: MATLAB Example
The symbolic toolbox can also be used.
This is especially useful for parametrized matrices (as in gain scheduling).
s = sym('s');
b = sym('b');
t = sym('t');
T = sym('T');
Ac = [0 0; b 1]; % b is a parameter
Bc = [1; 0];
% Do not use exp(Ac*T) to find A, since the exponential of a
% matrix has a different meaning in MATLAB.
At = ilaplace((s*eye(2)-Ac)^-1); % it will be a function of t
B = int(At*Bc, t, 0, T)
A = subs(At, t, T) % substitute t with T

## Slide 16: Conversions between CT and DT
In MATLAB, c2d and d2c may be used.
There are several possible conversion methods.
We have mentioned the zero-order hold method.
Other methods:
  First-order hold.
  Approximate differential equations as difference equations.
  The bilinear (Tustin) transformation.
  Matched pole-zeros.
  …

## Slide 17: Limitations
It is possible to convert a system from DT to CT or CT to DT.
  In MATLAB, c2d and d2c may be used.
However:
  The resulting systems are not equivalent in every respect to the original systems!
  Conversions should be used only when the theory permits them.

## Slide 18: Limitations—Example
Assume and .
In MATLAB, yields
Consider G in a feedback configuration with a proportional controller of value .
Considering , for stability or .
Considering , for stability or !

## Slide 19: Limitations—Example
Assume and .
Note the negative pole (without counterpart in the s-domain).
In MATLAB, yields
Consider G in a feedback configuration with a proportional controller of value .
Considering , for stability or .
Considering , there is instability for every !

## Slide 20: Designing SD Control Systems
A precise solution is to find the controller directly in the z-domain
  Use state estimation and state feedback.
  OR other methods.

## Slide 21: Designing SD Control Systems
A possible approach is to approximate a CT controller by a DT controller.
  First, find the controller C(s) in the s-domain.
  Then, approximate it by a DT controller.
  Approximations get better as .
There are several possible approximation methods.
  Find the differential equation representing and approximate it by a difference equation.
  OR use the formula
  OR use the bilinear transformation.

## Slide 22: Approximation by difference equations
Let
Analog PID controller
Digital PID controller

## Slide 23: Approximating State-Space Models
Consider a CT system with and its DT version .
Assuming the zero-order hold method:
, .
As , and .
Suppose that state feedback and state estimation place the poles so that CT poles and DT poles are related by .
As , .

## Slide 24: Approximating State-Space Models
As , .
Let and be the state feedback and estimation gains of the CT system.
As , and will ensure that the poles of the DT system are at the correct z-domain locations.
Notes: Sketch of proof: We will check that if is an eigenvalue of the CT system, then is an eigenvalue of the DT system. If , then . Moreover, if , then .
Sketch of proof: We will check that if 𝜆 is an eigenvalue of the CT system, then 1+𝜆𝑇 is an eigenvalue of the DT system. If (𝐴_𝑐−𝐵_𝑐 𝐾_𝑐 )𝑣=𝜆𝑣, then (𝐼+𝐴_𝑐 𝑇−𝐵_𝑐 𝑇𝐾_𝑐 )𝑣=(1+𝜆𝑇)𝑣. Moreover, if (𝐴_𝑐−𝐺_𝑐 𝐶)𝑣=𝜆𝑣, then (𝐼+𝐴_𝑐 𝑇−𝐺_𝑐 𝑇𝐶)𝑣=(1+𝜆𝑇)𝑣.