## Slide 1: Transfer-Function Based Analysis
Approximations, Jury’s Stability Test, Steady-State Response, Time Response
M.V. Iordache, EEGR4933 Automatic Control Systems, Spring 2019, LeTourneau University

## Slide 2: Designing SD Control Systems
A precise solution is to find the controller directly in the z-domain
  Use state estimation and state feedback.
  OR other methods.

## Slide 3: Designing SD Control Systems
A possible approach is to approximate a CT controller by a DT controller.
  First, find the controller C(s) in the s-domain.
  Then, approximate it by a DT controller.
  Approximations get better as .
There are several possible approximation methods.
  Find the differential equation representing and approximate it by a difference equation.
  OR use the formula
  OR use the bilinear transformation.

## Slide 4: Approximation by difference equations
Let
Analog PID controller
Digital PID controller

## Slide 5: Stability Calculations
The Routh-Hurwitz criterion may be used when z is substituted with
Alternatively, Jury’s test may be applied directly.

## Slide 6: Array for Jury’s Stability Test
Write the pole equation as Q(z) = 0 with
and an > 0. The array is:

## Slide 8: Stability Conditions
Notes: The first three conditions can be justified rather easily. From Vieta’s formulas, the product of the roots is , so we must have if the roots are inside the unit circle. Moreover, when varying on the real axis from to , will have sign changes, where is the number of real roots of . If all roots are inside the unit circle, then there must be no sign changes when varies from to , implying that must have the sign of , which is +; moreover, there will be no sign changes when varies from to , implying that must have the sign of . Now is an even number, since complex poles, if any, are in pairs. Therefore, . We conclude that we must have and .
The first three conditions can be justified rather easily. From Vieta’s formulas, the product of the roots is 〖(−1)^𝑛 𝑎〗_0/𝑎_𝑛, so we must have 𝑎_𝑛>|𝑎_0 | if the roots are inside the unit circle. Moreover, when varying 𝑧 on the real axis from −∞ to +∞, 𝑄(𝑧) will have 𝑚 sign changes, where 𝑚 is the number of real roots of 𝑄(𝑧). If all roots are inside the unit circle, then there must be no sign changes when 𝑧 varies from 1 to ∞, implying that 𝑄(1) must have the sign of 𝑄(∞), which is +; moreover, there will be no sign changes when 𝑧 varies from −∞ to −1, implying that 𝑄(−1) must have the sign of (−1)^𝑚 𝑄(1). Now 𝑛−𝑚 is an even number, since complex poles, if any, are in pairs. Therefore, (−1)^𝑚=(−1)^𝑛. We conclude that we must have 𝑄(1)>0 and (−1)^n 𝑄(−1)>0.

## Slide 9: Simplified Stability Test
Write the pole equation as Q(z) = 0 with
The array is:

## Slide 11: Stability Condition
For stability, an , bn-1 , cn-2 , … must not be zero and must have the same sign.

## Slide 12: Stability and the sampling period
An increase of the sampling period may result in instability (unless controller parameters are updated).
Exercise: Assume a discrete-time proportional controller in closed loop with the continuous-time plant . Given the control gain k, find the stability range of the sampling period T.
Notes: Note: The example assumes a ZOH that converts to continuous time the output of the controller.

## Slide 13: Steady-state calculations
Calculations can be simplified when the steady state is a constant.
  Ignore hold TFs.
  Replace G(s) (without the hold) with G(0).
  Replace H(z) with H(1).
  If G(0)/H(1) are undefined (), the steady-state input of G/H must be 0.

## Slide 14: Time Response
For pole placement, note the root locus and the curve of constant damping ratio.

## Slide 15: Time Response
The curve is almost linear near the (1,0) point.
  For small , poles will be close to (1,0).
  The linear region has a slope, as in the s domain.
Notes: % MATLAB code for the figure:
T = 0.01; zlist = [0.5, 0.7, 0.9];
subplot(1,2,1); wmax = 1000; w = 0:wmax/1e3:wmax; hold off;
for zeta = zlist
c = exp(w*T*(-zeta + sqrt(1-zeta^2)*1i));
plot(real(c), imag(c)); hold on;
end
grid on; legend('\zeta = 0.5', '\zeta = 0.7', '\zeta = 0.9'); axis square;
title('Curves of constant \zeta');
subplot(1,2,2); wmax = 10; w = 0:wmax/100:wmax; hold off;
xr = 0; yr = 1;
for zeta = zlist
c = exp(w*T*(-zeta + sqrt(1-zeta^2)*1i));
xr = max([xr, real(c(length(c)))]); yr = min([yr, imag(c(length(c)))]);
plot(real(c), imag(c)); hold on;
end
axis square; axis([xr 1 0 yr]); title('Close-up view');
grid on; legend('\zeta = 0.5', '\zeta = 0.7', '\zeta = 0.9');

## Slide 16: First-Order Systems
Assume a system of the form
The step response is similar to that of a continuous-time first-order system with a pole at .
The step response has a 2% settling time
  The approximation is good when is close to the unit circle.
  If is not associated with a sampled-data system, use and round the result to an integer.

## Slide 17: Second-Order Systems
Continuous time 2nd order systems have the form
The poles are .
Let .
A discrete-time system with poles at has the form

## Slide 18: Second-Order Systems
Given
The 2% settling time to a step input is
  is a pole of . The approximation is good if .
  If is not associated with a sampled-data system, use and round the result to an integer.
The percent overshoot could be approximated by the continuous-time overshoot:

## Slide 19: The Sample Period
Certain methods expect .
  If the signals have a max frequency , then should ensure the expected results.
About choosing a small T note that:
  The amount of computations is proportional to 1/T.
  Real-time constraints are harder to satisfy.
  The effect of quantization error can be very significant.
  Controller design: may have significant numerical error.
Controller parameters depend on T!